## TYPICAL SPECIFICATIONS FOR ACME

# GASPOST SENSOR / TRANSMITTERS

- Supply, install and connect as shown on drawings Acme GasPost Sensor/Transmitters.

- The GasPost shall be fully electronic utilizing advanced electrochemical sensor technology.

3.	The GasPost shall be housed in NEMA3 robust enclosures.

- The GasPost shall output 4-20mA on a 2-wire looped powered circuit. The GasPost shall also be available a 0-1V, 0-5V and 0-10V output version. The third version  of GasPost sensor/transmitter is available in RS485 addressable output version format compatible with the Acme CEL series equipment.

- The sensors shall measure PPM levels for all toxic gases and % for O2

- Standard threshold settings

| Table of factory default operating levels | FIRST ALARM SET POINT (LOW) | SECOND ALARM SET POINT (HIGH) | THIRD ALARM SET POINT (ALARM) | RADIUS OF COVERAGE |
| --- | --- | --- | --- | --- |
| Carbon Monoxide (CO) | 35 PPM | 100 PPM | 100PPM 30Min | 50 feet |
| Diesel (NO2) | 1 PPM | 2 PPM | 3PPM | 50 feet |
| Hydrogen (H2) | 800 PPM | 1300 PPM | 1800 PPM | 20 feet |
| Oxygen Deficiency (O2) | <19.5% | <18% | <17% | 20 feet |
| Ammonia (NH3) | 25 PPM | 35 PPM | 50 PPM | 20 feet |
| Hydrogen Sulfide (H2S) | 5 PPM | 10 PPM | 15 PPM | 20 feet |